## Slide 1: Things to do with the data

## Slide 2: Resolution - \20210525 fast pull back imaging resolution and aorta\20210519 side view data\wire phantom
For each image find the FWHM of the points circled, in both the lateral and axial dimension.
Make sure you find the FWHM of the Hilbert transformed data, but before log transform – you will need to change the script for this
Record: pull-back speed, repetition rate, depth of point, axial res, lateral res
Also find the signal to noise for the points (but this should be the 20*log10(abs(Hilbert(data))) – used the square box area to estimate noise level

## Slide 3: Resolution - \20210525 fast pull back imaging resolution and aorta\20210525 Fast motor imaging\resolution
Note there are two different a-line separations in this data set
For each image find the FWHM of the points circled, in both the lateral and axial dimension.
Make sure you find the FWHM of the Hilbert transformed data, but before log transform – you will need to change the script for this
Record: pull-back speed, a-line separation, repetition rate, depth of point, axial res, lateral res
Also find the signal to noise for the points (but this should be the 20*log10(abs(Hilbert(data))) – used the square box area to estimate noise level

## Slide 4: Aorta images: \20210525 fast pull back imaging resolution and aorta\20210525 Fast motor imaging\aorta
aorta
Side branch
Cork
For this data:
Reduce area plotted (still reconstruct the whole image, but make figure of just the green square)
Calculate SNR using the areas in the circles

## Slide 5: Aorta images: \20210525 fast pull back imaging resolution and aorta\20210525 Fast motor imaging\aorta
aorta
Side branch
Cork
For this data:
Reduce area plotted (still reconstruct the whole image, but make figure of just the green square)
Calculate SNR using the areas in the circles